## Slide 1: Development of a Smart Sensing System for Road Performance Data Collection
Victor Guerra, Michael Petersen, Ethan Young, Shlok Singh
Iowa State Program for Sustainable Pavement Engineering & Research (PROSPER)
Dr. Halil Ceylan, Bo Yang, Yueyi Jiao

## Slide 2: Project Plan
Ethan

## Slide 3: Problem Statement
Iowa DOT tracks road conditions
  Priority of road maintenance
Current solutions
  Laser rig: expensive, high maintenance
  Smartphone apps: proprietary, reliance on expensive hardware
Goal
  Cheap hardware & server for data collection & processing
Victor

## Slide 4: Project Overview
Road roughness gathering device
  Cheap implementation for Iowa DOT
  Comply with standard International Roughness Index (IRI)
Hardware
  Microcontroller with modules
  Black box that sits in a car on the dashboard above a wheel well
Software
  Upload raw data, convert to IRI, store, display to user
Ethan
Notes: Our project was tailored to the Iowa Department of Transportation.
Main emphasis is on the roughness of roads and creating a cheaper device to put in the fleet of vehicles that complies with the IRI standard.
To do this, we used h a microcontroller to place in the vehicles. This is a black box.
Software needs to be able to capture data from the shields on the arduino and integrate the data with the standard. This data will then need to be stored to be able to use later and display to users.

## Slide 5: Conceptual Sketch
Ethan

## Slide 6: Requirements - Functional
Device should collect accurate data
  GPS data
  Accelerometer data
  On the fly filtering for valid measurement conditions
Central server for large scale data processing
  Website file uploading
  GSM module
Proper data handling
  Server should be able to handle the load
Shlok

## Slide 7: Technical Constraint: Modelling Car
International Roughness Index (IRI)
  Widely adopted model
Quarter-car model
  Single tire model represents entire system
  Compliant to ASTM E1926-08
Golden Car
  Ratio of constants estimating typical vehicle
Victor

## Slide 8: Risks for Proposed Plan
Technical Risk
  Component communication issues
  Integration issues with public APIs
  Sample write speed to SD card; guarantee samples every 300mm
  Acceleration to position noise amplification
  Including libraries & embedded code on limited dynamic memory
  Consistent sampling for reasonable road profiles (time, speed)
Cost Risk
  Scaling cost
  Downtime cost/repair
Shlok
Notes: They dont work together, require the same pins/power
Code is not modular
write speeds slow
Data inaccuracy

## Slide 9: Risk Management
Technical Risk
  Well-documented hardware components
  Scaled down shield libraries to essential functions
  Significant experimenting with sample rate consistency
  Selective GPS polling for quicker sampling
  Filtering methods during data processing
  Filtering methods during data collection
Cost Risk
  Lightweight scalable back end
  Readily available hardware
Shlok

## Slide 10: Cost Breakdown
Resource Name | Cost
Arduino Uno | $20.50
Arduino Battery (3.7V 1200mAh) | $9.95
Accelerometer Module (LSM9DS1) | $15.95
SD card module | $4.99
GSM Shield | $49.95
SIM Card + Data Plan | $9.00 + Data plan
GPS & GSM antenna | $2.95
microSD card (8GB) | $6.75
Azure Web Server (IowaDOT can use own servers) | Varies based on devices used -- used student credit for prototyping
Total Device Cost | ~$120
Mike

## Slide 11: II. System Design
Ethan
Notes: Next, we will get into the design of our prototype that we created.

## Slide 12: Functional Decomposition
Ethan
Notes: This is basically how the data flows through the system for the prototype.
Data is captured on the black box and stored to the SD card.
From here, the data is parsed on the server, processed, and sent to the database.
Once in the database, the front-end can get ahold of the stored IRI values and display them for the users.

## Slide 13: System Design (Arduino)
Arduino Uno
Factors in microcontroller selection
  Power Consumption
  Pin availability
  IO availability
  Processing power
  Available software libraries
  Available memory
Capturing raw data on SD Card
Mike

## Slide 14: Flow Diagram
Mike

## Slide 15: System Design (Back-End)
Azure Web Server running Apache
  Node service
  MySql database
Javascript Modules
  Parsing raw data files
  Integration of acceleration values
    Trapezoidal Riemann Sums
    Filtering due to quadratic error
  IRI calculation
    ASTM E1926-08 compliance
Ethan
Notes: The back-end was made to be functional on an Azure Web Server running Apache.
This Azure server included a Node service to control the data and a MySQL database to store the data.
After a file is uploaded, the parser would parse it to a readable format for the data processing.
After parsing, the data is given to the DataController which feeds the integration and the IRI calculation.
The data is first given to the DataIntegration module where it is integrated from accelerometer data to positional profile.
During the integration, we also used a kalman filter to filter the data to reduce noise and quadratic integration error.
The positional profiles then go to the IRI calculation module which gets the IRI value.
The controller then throws this data along with gps coordinates and speed into the database.

## Slide 16: System Design (Front-End)
Front-end file upload
  Upload data files from Arduino
  Multiple uploads at once
  Used React-Files for drag and drop and file search features
Front-end data retrieval
  Requests database from Node server
  Displays in a table
Ethan
Notes: The front-end is essential to upload the files from the SD card on the Arduino. It is created in a way to allow for multiple uploads at one time as well.
I used a publicly available component as a dependency for the file selection process called react-files. This just allows to drag and drop files or to click on it and get presented with a file explorer to locate the file.
There is also a table on here that just contains everything that is stored in the database. This data would be mapped out with a map api, but we were unable to achieve this goal in time. It was a stretched goal that we had in the initial planning phase that we were going to get to if we got the main requirement done early.

## Slide 17: Test Process
Limited by access to PROSPER equipment
  Nothing to compare results with
Accelerometer Z-axis expectations
  Centered around 1 g-force
  Not logging when travel speeds aren’t constant
Road sample IRI profiles plotted expectations
  Roughly 0 slope for average roads
  Values ~0<avg<3 smooth roads, ~ <10 rough (speed dependent)
  Filtering methods to reduce extreme data points
  High speeds => lower IRI values
Victor

## Slide 18: Integration Tests
Hardware shields on Arduino
  Individually and together
Embedded code on Arduino
  Log compatibility with back-end parser
Back-end server
  Postman test requests
Front-end upload and data retrieval
  Verify operation with back-end
Ethan
Notes: For the integration testing, we first made sure the hardware would integrate together file. So we tested the shields individually and then all together before we made any soldering decisions.
To make sure that the arduino code would integrate with the backend, we made sure that the files stored on the SD card were compatible with the backend for every change we made.
Postman was also used for the backend to make sure that the API worked as intended and responded with the correct results.
The front-end client was primarily tested to make sure that the data and http requests were working as intended and that there was no loss of data when transering

## Slide 19: Testing Challenges
GSM HTTP packets malformed/blank
Sample rate inconsistency
GSM communication establishment time
Accelerometer dynamic positioning
Limited on-board memory
Shlok

## Slide 20: Final Implementation
Victor

## Slide 21: Test Results - Accelerometer Data
Accelerating to cruise control @ ~73kph
~3 minute drive @ variable speeds, note noisiness at end
Victor

## Slide 22: Test Results - IRI Calculation: Loose XY
Victor

## Slide 23: Test Results - IRI Calculation: Final XY
Victor

## Slide 24: Engineering Standards and Design Practices
ASTM E1926-08: Standard Practice for Computing International Roughness Index of Roads from Longitudinal Profile Measurements
RFC 2616: Hypertext Transfer Protocol -- HTTP/1.1
ECMA-404: The JSON Data Interchange Syntax
Real-time operating system (RTOS) for small-scale embedded systems
Agile-like environment with Kanban elements for software development process
Mike

## Slide 25: III. Conclusions
Ethan
Notes: Now we will go into some conclusive remarks about the project.

## Slide 26: Considerations, Lessons Learned
GPRS is tricky
  Failed to build proper HTTP packets, unable to deliver wireless option for raw data transfer
Budget components may lack critical features
  Specifically, accelerometer for positional awareness
  Budget GPS device with questionable connectivity
  2G transfer speed unreliable, future iterations should consider budgeting for 3G or 4G
Filtering parameters (XY, OOB acceptance, filter noise level) need calibration against real world data
Ethan
Notes: We learned that the gprs was tricky to get going. The body of the http requests were always blank and we could not find another library that was compatible with our hardware.
The budget components may also lack some critical features that we need for more precise calculations. specifically components such as the accelerometer with dynamic collaboration, gps device, and especially the gsm module with only having 2g speeds.
We may also need to tweak many of the filtering parameters that we are currently using such as what is considered out of bounds via the XY acceleration as well as the kalman filter with its noise level. We would definitely need some real world data to test against to make sure that it is accurate.

## Slide 27: Contributions
Shlok Singh
    Back-end, Networking
Ethan Young
    Hardware Setup, Front-end, Back-end
Victor Guerra
    Physics, Embedded design, Data processing
Michael Petersen
    Embedded design, Testing
Mike

## Slide 28: References
http://onlinepubs.trb.org/Onlinepubs/trr/1989/1215/1215-018.pdf
https://www.hindawi.com/journals/mpe/2014/928980/
https://www.sparkfun.com/pages/accel_gyro_guide
https://media.ford.com/content/dam/fordmedia/Europe/en/2016/02/worst_potholes_EU_7.pdf

## Slide 29: Market Survey
Current Iowa DoT data collection : High Cost - High Accuracy

## Slide 30: Conceptual Need
Target clientele: Iowa DOT maintenance analysts
Affordability
Reliability
Standardized roughness model
Scalable

## Slide 31: Project Deliverables
Data gathering on Arduino
  Accelerometer, speed, GPS, time
Data storing on Arduino
  SD Shield
Uploading data containence to cloud server
  Web client to database
Displaying data on front-end web client
  React website

## Slide 32: Requirements - Non-Functional
Reasonable cost (~$100)
Minimal user interaction
Weather resistance
Rugged design

## Slide 33: System Design Overview
Black Box enclosure
  Microcontroller
    Accelerometer
    GPS
    Removable storage
    GSM
Data server
Web client application

## Slide 34: Test Process
System Tests:
  Plotting final IRI measurement vs. related parameters
  Module and Component testing
    Individual, integrating multiple together
    Local machine
  HTTP requests & handling efforts
    Postman
Unit Tests:
  ASTM E1926-08 compliance sample data for profile to IRI
  Javascript module testing

## Slide 35: Challenge Solutions & Failures
Technical Challenges
  Smaller than desired sample sizes, still allows calculation
  Device not suited for hilly areas
  Library customization to save memory space

## Slide 36: Test Results - Filtering

## Slide 37: Test Results - Distance vs. Speed for Sample

## Slide 38: Test Results - Unpaved Road ~55kph

## Slide 39: Timeline